## Slide 1: Deep Learning Techniques for Gesture Recognition: Where to Split the Complexity
Matteo Drago, Riccardo Lincetto
Dept. of Information Engineering, University of Padova, Italy
Prof. Michele Rossi
September, 5, 2018
matteo.drago@studenti.unipd.it
riccardo.lincetto@studenti.unipd.it

## Slide 2: Outline
mmWave Cellular Networks
Proposed architecture
Performance evaluation
  ns-3 mmWave module
  Results
Conclusions

## Slide 3: 3GPP New Radio
New RAN
  OFDM-based PHY with flexible configurations
  Support for
    Higher frequencies (mmWaves)
    Ultra-low latency
New Core Network
  Softwarization of network nodes
  Network slicing

## Slide 4: mmWave for the mobile RAN
Potentials
  Bandwidth
  Large arrays in small space
Challenges
  High propagation and penetration loss
  Directionality
  Blockage
3GPP Rel. 15 supports carrier frequency up to 52.6 GHz

## Slide 5: Applications
Ultra-high quality video streaming and VR are seen as possible use cases of 5G
How can we stream high quality video to mmWave users?

## Slide 6: Related work
IEEE 802.11ad solutions for VR and streaming in local networks
  Very different setup from cellular networks [1]
LTE streaming solutions
  Different frequency bands and less demanding propagation conditions
  Also using network coding [2]
[1] O. Abari, D. Bharadia, A. Duffield, and D. Katabi, “Enabling high-quality untethered virtual reality,” in 14th USENIX Symposium on Networked Systems Design and Implementation (NSDI 17). USENIX Association, pp. 531–544
[2] D. Vukobratovic, C. Khirallah, V. Stankovic ́, and J. S. Thompson, “Random Network Coding for Multimedia Delivery Services in LTE/LTE- Advanced,” IEEE Transactions on Multimedia, vol. 16, no. 1, pp. 277– 282, January 2014

## Slide 7: mmWave Video Streaming Architecture
Application layer solution implemented in Mobile Client and Video Streaming Server (VSS)
Multi connectivity
Network coding

## Slide 8: Multi connectivity in mmWave networks
Increases resiliency and improves end-to-end performance
  Combine links at different frequencies
  In the RAN [1] (LTE-NR Dual Connectivity, Carrier Aggregation)
  At the transport layer (Multipath TCP [2])
[1] M. Polese, M. Giordani, M. Mezzavilla, S. Rangan, and M. Zorzi, “Improved Handover Through Dual Connectivity in 5G mmWave Mobile Networks,” IEEE Journal on Selected Areas in Communications, vol. 35, no. 9, pp. 2069–2084, September 2017.
[2] M. Polese, R. Jana, and M. Zorzi, “TCP and MP-TCP in 5G mmWave Networks,” IEEE Internet Computing, vol. 21, no. 5, pp. 12–19, September 2017.

## Slide 9: Multi connectivity for video streaming
We exploit multi connectivity at application layer
  LTE: low rate, high reliability
  mmWave: high rate, lower reliability
LTE is used also to provide feedback from the user to the VSS
Video Encoder
IP
UDP
IP
UDP
Video Distribution Layer
LTE
mmWave

## Slide 10: Network coding
Combine packets with algebraic operations to increase resilience
Random Linear Network Coding with Kodo [1]
  Good bandwidth efficiency, complexity and latency
  Operates on Galois field with elements
  Rateless approach
    Combine source packets into coded packets
    Decode from any set of linearly independent packet combinations
[1] http://docs.steinwurf.com/overview.html#kodo
Notes: Non serve andare troppo nei dettagli

## Slide 11: Network coding for video streaming
Powerful combination with multi connectivity
  No HoL blocking issue
  Retransmit new encoded packets on any interface
Trade offs between
  Latency and decoding probability (both increase with )
  Decoding complexity and decoding probability (both increase with )
LC configuration , Lower latency Lower decoding probability | HC configuration , Higher latency Higher decoding probability

## Slide 12: Video encoding
H.264 with Scalable Video Coding extension
Temporal layers
  Frames with different importance in temporal domain
Spatial layers
  Encode different resolutions in the same bit stream

## Slide 13: Realistic video streaming extension
We simulate the streaming, buffering and play-out of video frames from a real video
Tools
  JSVM to extract the H.264 bitstream
  FFmpeg for video decoding and quality evaluation
  Custom SVEF extension for adaptation of the bistream to ns-3
Notes: Non entrare troppo nei «dettagli di codice» ma fare ad esempio un’immagine/diagramma a blocchi per rappresentare i diversi step eseguiti

## Slide 14: Simulation scenario
Comparison between
  LC and HC network coding setups
  Retransmission policies
    RAN retransmissions (HARQ and RLC AM)
    Network coding FEC
UE
UE
Obstacle

## Slide 15: End-to-end latency and NALU* loss
Latency
NALU loss
Multi connectivity yields the largest gain
Without multi connectivity, NC performs better for NALU loss at the cost of higher latency
*NALU: portion of the video bitstream mapped to a network packet
Notes: Latenza elevata dovuta alla richiesta di un numero più alto di pacchetti codificati

## Slide 16: PSNR
Inversely proportional to MSE between received and transmitted frame, maximum value with FFmpeg 99.99 dB
Lower latency
Higher video quality
Proposed solution with multi connectivity and network coding

## Slide 17: Conclusions
Video streaming architecture for mmWave networks
Evaluated with realistic ns-3 mmWave and video streaming model
Improved video quality with low latency
  Useful for high quality live streaming
Important interplay between multi connectivity and network coding
Future work
  Implementation of NOW and EW approaches

## Slide 18: Reliable Video Streaming over mmWave with Multi Connectivity and Network Coding
Matteo Drago*, Tommy Azzino*, Michele Polese*,
Cedomir Stefanovicv, Michele Zorzi*
*Dept. of Information Engineering, University of Padova, Italy
VAalborg University, Copenhagen, Denmark
April, 27, 2018
matteo.drago@studenti.unipd.it
tommy.azzino@studenti.unipd.it
mmwave.dei.unipd.it